## Slide 1: FerroDyn PML Tests
Test #1 – Benchmark test problem from Chew & Weedon (1994).
Case setup: Free-space discretized using a 3D grid of size 128x128x32, with an electric dipole generating a time-dependent source pulse. The domain is enveloped by PML boundaries on all sides to model free-space.
Electric field is sampled at a point sufficiently distant from the point source and plotted over time.

## Slide 2: Test #2
Case setup: An infinitesimal light source is placed at the center of a cubic domain, with PML boundaries on all sides. Increasing the domain size, while keeping the source at the center, should preserve the E field profile at a fixed distance from the source.
In simpler words, the E field at a distance x from the source should remain invariant as the domain size changes.

## Slide 3: Test #3
Dielectric with isotropic permittivity
Planar current source
Both the PML and the ABC should work in this case
x
2 | 0 | 0
0 | 2 | 0
0 | 0 | 2
Relative permittivity
 | E_x | E_y | E_z | H_x | H_y | H_z
Average Relative Error | 2.24704e-05 | 0.0 | 0.0 | 0.0 | 7.27529e-05 | 0.0
Black line represents wave amplitude including the solution within the PML region.
Purple lines (overlapping) represent the wave amplitude in the physical domain.

## Slide 4: Test #4
Dielectric with anisotropic permittivity
Planar current source
PML is needed to ensure that there is no EM wave reflection from the corner
2 | 0 | 0
0 | 8 | 0
0 | 0 | 8
Relative permittivity
 | E_x | E_y | E_z | H_x | H_y | H_z
Average Relative Error | 1.27162e-05 | 9.14771e-06 | 0.0 | 9.70195e-05 | 6.97178e-05 | 0.0

## Slide 5: Test #5
Dielectric with either isotropic or anisotropic permittivity
Planar current source
PML is needed to ensure that there is no EM wave reflection from the corner
wavevector
2 | 0 | 0
0 | 2 | 0
0 | 0 | 2
Relative permittivity
 | E_x | E_y | E_z | H_x | H_y | H_z
Average Relative Error | 1.25257e-05 | 8.78869e-13 | 3.58303e-06 | 5.0e-01 | 7.2888e-05 | 7.31158e-04
4x4x100
Dielectric is at z = 30-60.
Planar current source is at z = 20